## Slide 1
Home Automation
Making Smart Homes Smarter

## Slide 2
Introduction:
What is Home Automation?
Brief overview of the project's aim
Home automation refers to the use of technology to control and monitor household systems and appliances automatically or remotely. It allows homeowners to manage lighting, climate, entertainment systems, security, and more using smartphones, computers, or voice commands.
This project focuses on creating a smart home system using Arduino and cloud computing technologies. The primary goal is to control home appliances remotely and monitor real-time data (like temperature, motion, etc.) via a smartphone or web interface.

## Slide 3
Objective of the project
✅ Remote Control of Appliances
📱 User-Friendly Interface
🌐 Cloud-Based Monitoring
Allow users to turn ON/OFF lights, fans, and other devices from anywhere using a smartphone or web interface.
Integrate with platforms like Blynk, Arduino IoT Cloud, or a custom web dashboard for easy access and control.
Send real-time data from sensors (like temperature or motion) to the cloud for live monitoring and data logging.

## Slide 4
  Arduino UNO/Nano
  Relay Module
  Sensors (DHT11, PIR, etc.)
  Wi-Fi Module (ESP8266)
Components
Hardware
Software
  Arduino IDE
  Arduino IoT Cloud
  IFTTT

## Slide 5
Architecture
  Arduino IDE
  Arduino IoT Cloud
  IFTTT

## Slide 6
Code/Working
#include <DHT.h>
#include <ESP8266WiFi.h>
#include <ESP8266HTTPClient.h>
#include "thingProperties.h"
#define DHTPIN 2 // D4 on NodeMCU
#define DHTTYPE DHT11
#define LEDPIN 5 // D1 on NodeMCU
DHT dht(DHTPIN, DHTTYPE);
void setup() {
Serial.begin(9600);
delay(2000);
Serial.println("Initializing...");
initProperties(); // Arduino IoT Cloud properties
pinMode(LEDPIN, OUTPUT);
dht.begin();
delay(2000); // Give DHT time to stabilize
ArduinoCloud.begin(ArduinoIoTPreferredConnection);
setDebugMessageLevel(4);
ArduinoCloud.printDebugInfo();
Serial.println("Setup complete.");
}
void loop() {
ArduinoCloud.update();
readSensor();
}
void readSensor() {
Serial.println("Reading sensor values...");
float t = dht.readTemperature();
float h = dht.readHumidity();
if (!isnan(t)) {
temp = t;
Serial.print("Temperature: ");
Serial.print(temp);
Serial.println(" °C");
if (temp > 30) {
sendToIFTTT(temp);
}
} else {
Serial.println("Failed to read temperature");
}
if (!isnan(h)) {
humid = h;
Serial.print("Humidity: ");
Serial.print(humid);
Serial.println(" %");
} else {
Serial.println("Failed to read humidity");
}
delay(5000); // Delay between readings
}

## Slide 7
Advantages
  Energy efficiency
  Convenience and comfort
  Enhanced home security
  Scalable and customizable

## Slide 8
Features
  Remote control of home devices
  Real-time temperature & humidity display
  Motion detection alerts
  Voice control (if integrated with Alexa/Google)

## Slide 9
OUTPUT